## Slide 1: B.Tech – BCSE497J REAL-TIME CROWD TURBULENCE AND STAMPEDE HAZARD PREDICTION IN PUBLIC INFRASTRUCTURE
Team members:
Kadali Navneet Sai (Reg. No. 23BCI0098)
Korupolu Manudeep (Reg. No. 23BCE0429)
Boddu Vinesh (Reg. No. 23BDS0138)
Faculty guide :
Dr. Kopperundevi N

## Slide 2: Aim
To design and deploy a real-time, edge-AI crowd monitoring system on a low-power embedded camera (Realtek AmebaPro2, RTL8735B NPU) that detects people and estimates crowd density in public infrastructure such as railway stations, stadiums, and religious gatherings — running a quantized YOLO26 model fully on the onboard VIP8000 Nano NPU so raw video never leaves the device (privacy-preserving edge inference).
To convert per-frame detections into a persons-per-m² density heatmap and, using optical-flow crowd-motion cues (speed variance, flow direction, counter-flow), compute a turbulence/hazard score over high-risk chokepoint and region-of-interest zones (gates, staircases, platforms).
To stream live, detection-annotated video to a remote control room over AWS Kinesis Video Streams (KVS) WebRTC for secure, low-latency verification, and to push AWS IoT / MQTT alerts to operators the instant a hazard threshold is crossed.
To raise tiered early-warning alerts (Normal / Caution / Critical) before a stampede-prone condition develops, and log density/flow metrics on-device for post-event review and venue capacity planning.

## Slide 3: Abstract
Public gatherings at railway stations, stadiums, religious events, and other high-footfall infrastructure are increasingly prone to stampede incidents caused by sudden crowd turbulence, chokepoints, and delayed situational awareness; conventional CCTV monitoring relies on manual observation or cloud-only analytics, both of which add latency and scale poorly.
This project presents a real-time, edge-AI crowd monitoring system on the Realtek AmebaPro2 (RTL8735B) embedded camera: a lightweight YOLO26 detection model, quantized for the onboard VIP8000 Nano NPU, performs on-device person detection and a persons-per-m² density estimate without offloading raw video to the cloud (privacy-preserving edge inference). Density is fused with optical-flow crowd-motion cues speed variance and counter-flow across chokepoint/ROI zones into a turbulence/hazard score that drives tiered early-warning alerts (Normal/Caution/Critical).
Detection-annotated video is streamed live via AWS KVS WebRTC to a control-room viewer with sub-second latency, and AWS IoT / MQTT alerts are pushed to operators the moment a threshold is crossed reducing bandwidth and cloud dependency while enabling faster, proactive stampede-risk response and on-device logging for post-event review.

## Slide 4: Literature Review
Paper | Objective | Methodology | Pros / Cons | Findings
CrowdSentry (2025) | Stampede-risk prediction at railway stations | YOLOv8 + Deep SORT tracking on calibrated spatial grids | + Real per-m² density – Needs GPU server | Density grid predicts stampede risk zones
YOLOv8 + Spatio-Temporal Modeling (2025) | Predict stampede probability from video | YOLOv8 detection fused with motion/behaviour features | + Captures crowd motion – Offline evaluation only | Stampede probability score per clip
Intelligent Crowd Monitoring (YOLOv8m+CNN-LSTM, 2026) | Early warning for stampede-prone crowds | YOLOv8m detection + CNN-LSTM temporal model | + Temporal awareness – Heavy for edge devices | Early-warning alerts on abnormal flow
Crowd Density Monitoring (IJERT, 2026) | Real-time density monitoring & prevention | Classical CV + deep learning density pipeline | + Simple, fast – No edge/NPU deployment | Threshold-based crowd alerts
Thermal-Camera Stampede Risk (IEEE, 2025) | Density estimation independent of lighting | Thermal imaging + risk-assessment algorithm | + Works in low light – Loses visual/box detail | Comparable density accuracy to RGB
YOLO-Based Real-Time Crowd Detection (2023) | Compare YOLO models for crowd detection | Benchmarks YOLO variants on crowd video | + Real-time on GPU – No edge/quantization study | Guides YOLO choice for crowds
YOLO-CROWD (YOLOv5s, 2023) | Lightweight crowd counting on edge devices | YOLOv5s-based detector, 18.4M params | + 10.1 ms/frame on edge – No streaming pipeline | Edge-feasible but not NPU/quantized
Dense Optical-Flow Stampede Detector (2025) | Detect stampede onset in low/medium crowds | Gunnar-Farneback dense optical flow + deep learning | + Motion-based, real-time – Sensitive to camera shake | Reliable stampede-onset detection
CNN-LSTM + Farneback Flow (Sci. Reports, 2026) | Stampede detection & crowd-risk classification | Farneback optical flow fused with CNN-LSTM | + Spatio-temporal risk classes – GPU training cost | Risk levels on UCSD/Agoraset data
Edge-SoC Detection Benchmark (Sci. Reports, 2026) | Guide YOLO deployment on edge SoCs/NPUs | Reproducible ONNX→quantize→compile NPU benchmark | + Practical deploy guidelines – Not crowd-specific | Quantized YOLO viable on edge NPUs
Q-YOLO (2023) | Efficient real-time detection via quantization | Post-training quantization, histogram activation ranges | + Near-FP accuracy at low bits – PTQ tuning needed | Low-bit YOLO retains accuracy
Crowd Counting on NPU Platform (CMC, 2023) | Deploy crowd counting on an NPU device | Deep density-map CNN ported to NPU hardware | + On-device counting – Density-map only, no boxes | Real-time NPU crowd counting feasible
CSRNet + Attention for Transit (2026) | Crowd counting in public transport | Dilated-CNN CSRNet with parameter-free attention | + Accurate in congestion – Heavy for MCU-class NPU | Improved MAE on transit crowds

## Slide 5: Research Gap
Existing YOLO with spatio-temporal stampede-prediction pipelines are validated mostly on GPU workstations or offline datasets, not on power-constrained embedded NPUs; edge-board implementations (e.g. Jetson-class) still stream raw video to a central server, adding latency, bandwidth cost, and privacy exposure that limit scale across venues with hundreds of cameras.
Optical-flow / thermal / IoT-sensor approaches either need heavy compute or sacrifice the rich visual context (individual bounding boxes, occlusion handling) that vision-based YOLO detectors provide and few fuse detection density with motion cues into a single actionable hazard score.
No reviewed system combines (a) fully on-device, privacy-preserving NPU inference on a cheap embedded camera, (b) standards-based low-latency WebRTC streaming via AWS KVS with IoT/MQTT alerting for remote verification, and (c) a pipeline explicitly aimed at stampede/turbulence-hazard prediction with tiered early-warning rather than generic people counting.
Chokepoint/ROI-aware density-and-flow analysis (persons-per-m² heatmaps, counter-flow detection) is rarely delivered at the edge in real time on constrained hardware.
Quantization-induced accuracy loss when compressing YOLO models for embedded NPUs (e.g. uint8 dynamic-range collapse of the confidence/box outputs) is rarely addressed in the crowd-safety literature, despite being a key real-world deployment blocker.

## Slide 6: Objectives
Deploy a quantized YOLO26 model on the AmebaPro2 RTL8735B VIP8000 NPU for real-time (≥15 FPS), privacy-preserving on-device person detection.
Compute a frame-wise persons-per-m² density metric and heatmap, focused on chokepoint / region-of-interest zones (gates, staircases, platforms).
Fuse density with optical-flow motion cues (speed variance, counter-flow) into a turbulence/hazard score with tiered (Normal/Caution/Critical) early-warning.
Stream detection-annotated video via low-latency AWS KVS WebRTC and push AWS IoT / MQTT alerts to operators on threshold crossings.
Evaluate quantization trade-offs (uint8 vs. int16) to balance model size, speed, and confidence precision on the NPU; log density/flow metrics for post-event review.
Identified SDG 9 and SDG 11 as the primary SDGs relavant to the project.

## Slide 7: References
[1] "CrowdSentry: An AI-Powered Framework for Realtime Crowd Behavior Analysis and Stampede Risk Prediction," IEEE Conf. Publication, 2025.
[2] "Real-Time Stampede Risk Prediction from Crowd Videos Using YOLOv8 and Spatio-Temporal Modeling," 2025.
[3] "Real-Time Crowd Density Monitoring and Stampede Prevention Using Computer Vision and Deep Learning," Int. J. Eng. Res. Technol. (IJERT), vol. 15, no. 4, 2026.
[4] "Intelligent Crowd Monitoring and Early Warning Framework for Stampede Prevention Using YOLOv8m and CNN-LSTM Architecture," Int. J. Comput. Trends Technol. (IJCTT), vol. 74, no. 6, 2026.
[5] "Real-Time Crowd Density Estimation and Stampede Risk Assessment System Using Thermal Camera," IEEE Conf. Publication, 2025.
[6] "A New YOLO-Based Method for Real-Time Crowd Detection From Video and Performance Analysis of YOLO Models," 2023.
[7] O. Zaki, "YOLO-CROWD: A Lightweight Crowd Counting and Face Detection Model Based on YOLOv5s," GitHub repository, 2023.
[8] "Stampede Detector Based on Deep Learning Models Using Dense Optical Flow," Engineering Applications of Artificial Intelligence, Elsevier, 2025.
[9] "Stampede Detection and Crowd Analysis Using CNN-LSTM and Farneback Optical Flow," Scientific Reports, Nature, 2026.
[10] "Object Detection on Low-Compute Edge SoCs: A Reproducible Benchmark and Deployment Guidelines," Scientific Reports, Nature, 2026.
[11] "Q-YOLO: Efficient Inference for Real-Time Object Detection," arXiv:2307.04816, 2023.
[12] "A Deep Learning-Based Crowd Counting Method and System Implementation on Neural Processing Unit Platform," Computers, Materials & Continua (CMC), vol. 75, no. 1, 2023.
[13] "Optimising CSRNet with Parameter-Free Attention Mechanisms for Crowd Counting in Public Transport," arXiv, 2026.